Barber Mod PCB manual.

Note Shape- takes the bass strings from snappy and tight, to big, round and vintage. (stock is 9 o’clock)

Harmonics- adjusts secondary harmonic generator, stock is about 11 o’clock. This control is not added to the LTD, and is already on DDSS units.

Switch:

1. Gain-this switch activates the higher than stock Gain mode, this creates much greater sensitivity. High gain is activated when this rocker is pressed down toward the #1.

2.  Asymmetry 1-this switch activates a vintage compressed asymmetry and is activated when the rocker is pressed down toward the #2.

3. Asymmetry 2 -This switch activates the lowest compression mode, although it creates a slight asymmetry good for cutting through with thick sounding humbuckers and P90 style pickups cool with single coils too! Asym is activated when the rocker is pressed down away from the # 3.

4. Fizz filter bypass- This switch hard bypasses the fizz filter control. The fizz filter is activated when the rocker is pressed down toward the #4.

------------------------------------------------------------------------------------------------------------

Midrange adjust- this control adjusts the midrange content of your pedal, stock is about 12 o’clock.

Fizz Filter- this control allows you to tame the unwanted fizzy treble content that some vintage style speaker designs can impart at lower volumes, this control is activated and turned off by the fizz filter switch for convenience.

Questions?

717-630-9191

david@barberelectronics.com